## Slide 1
BY
Name:
Des
Inst

## Slide 2: Review Previous Session :
Perform pigtail joint
These question does not appear in the slide
What is bare wire
Why it is called pigtail joint
What amount of insulation should be removed

## Slide 3: To-Day’s Learning Outcome
At the end of this session you will be able to perform western union joint perfectly within ten (10) minutes as per industry standard.

## Slide 4
Structure
(Introduction, Discussion, Demonstration, Practice Session, Review & Feedback, Next Session )
&
Stimulation

## Slide 5: Structure & Stimulation

## Slide 7: Required Equipment
Sl. No. | Tools and Equipment | Quantity
1 | Wire stripper | 1 unit
2 | Needle nose pliers | 1 unit
3 | Cutting pliers | 1 unit
4 | Insulating tape | 1 unit
Sl. No. | Raw Materials | Quantity
1 | Cable (1.0 Re) | 1 coil

## Slide 8: Western Union Joint
The Western Union splice or joint is a method of joining electrical cable.
It is developed in the nineteenth century by the telegraph company named Western Union telegraph company.
This method can be used where the cable may be subject to loading stress.
The wrapping pattern design causes the join to tighten as the conductors pull against each other.
Fig: Western Union Joint

## Slide 9: Procedure
The Western union splice is made by twisting two ends of a wire together counterclockwise 2 or 3 of a turn each, finger tight.
First remove 2 to 3 inches insulation from each cable by using wire stripper.
Collect the cables which have to make joint.
Fig: Remove insulation
Fig: Twisting wire

## Slide 10: Procedure (Contd.)
After tighten, the joint area must covered with insulation tape.
Then, using needle-nose pliers, the ends are twisted at least four (4) more turns, tightly.
Fig: Taping the Twisted area
Fig: Tighten the twisted wire

## Slide 11: Demonstration
Wear PPE
Take job sheet and specification sheet
Take tools and equipment
Step-1. Do it normal
Step-2. Do it slow
Step-3. Do it Together
Practice Session

## Slide 12: Review and Feed Back
What we learned from this session:

## Slide 13: If You Can Perform This Joint Then-
You can apply in your practical life
You can make a joint of overhead transmission line as it is a very strong joint.
You can extent wire, conductor or cable.

## Slide 14: Next Session
Perform T-joint
T-joint
CBLM-9, Page-27

## Slide 15: Thank You